## Slide 1
MDM CAPSTONE · AI + IOT
SITEGUARD
AI-Based Construction Site Worker Safety Monitoring System
Real-Time Edge Ingestion • YOLOv8n PPE Detection • BoT-SORT Deep Re-ID • Temporal Hysteresis Rule Engine
ESP32-CAM (5 FPS)
YOLOv8n (640x640)
BoT-SORT Re-ID
70/30 Hysteresis
SQLite WAL Mode
WebSocket Dashboard

## Slide 2
02 · CONTEXT & STRATEGY
The Problem & Core Project Objectives
SITEGUARD · 02
Construction Safety Challenges
20%+ OF ALL WORKPLACE FATALITIES OCCUR IN CONSTRUCTION
Missing hardhats & safety vests is the #1 cited OSHA violation nationwide.
• Low PPE Compliance: Workers frequently remove helmets and vests in unsupervised zones when no officer is present.
• Monitoring Fatigue: Safety supervisors cannot watch multiple live camera feeds continuously; human lapses occur.
• False-Alarm Fatigue: Raw single-frame detectors flicker heavily on momentary occlusion and noise, causing alert dismissal.
• Machinery Blind Spots: Ground workers cross paths with excavators and cranes without spatial danger tracking.
Five Core Objectives
✔ 01. Edge Video Ingestion Stream low-latency QVGA/VGA frames from wireless ESP32-CAM nodes over Wi-Fi at 5 FPS pacing.
✔ 02. Accurate PPE Attribution Simultaneous detection of workers and safety gear with strict bounding-box containment (IoU >= 0.50).
✔ 03. Stable Identity via Re-ID Keep worker IDs consistent through visual occlusions and intersecting paths using BoT-SORT appearance vectors.
✔ 04. Zero Alert Flapping Confirm violations only when missing in >=70% of frames over a 10s window (clear at <=30%).
✔ 05. Real-Time Operations Instant WebSocket alert broadcast, evidence JPEG snapshots, and SQLite WAL database audit logging.

## Slide 3
03 · SYSTEM DESIGN
Core Features & 8-Stage End-to-End Architecture
SITEGUARD · 03
Key System Capabilities
• Multi-Camera Ingestion: Raw JPEG HTTP POST from wireless ESP32-CAMs & webcams.
• Domain PPE Detection: Person, Hardhat, Vest, Mask & their 'NO-' violation states.
• Tracking & Re-ID: BoT-SORT appearance embeddings (ByteTrack supported).
• Spatial Containment: >=50% box overlap ties gear strictly to wearer body.
• Temporal Hysteresis: 10s window, 70% confirm / 30% clear eliminates flickering.
• SQLite WAL Engine: High-concurrency, non-blocking ACID incident logging.
• WebSocket Hub: Real-time alert dispatch to web dashboard in sub-50 ms.
• Diagnostics & Telemetry: ESP32 RSSI, heap, FPS tracking; offline after 15s.
8-Stage Frame Dataflow Pipeline
1. Ingestion
ESP32-CAM posts raw JPEG @ 5 FPS via HTTP POST
[routes/camera.py]
2. Preprocessing
BGR to LAB, CLAHE on L channel (<4.2 ms), Letterbox 640x640
[preprocessor.py]
3. Detection
YOLOv8n finds Person, PPE worn & missing, and machinery
[inference.py]
4. Re-ID Tracking
BoT-SORT preserves worker track IDs across visual occlusions
[botsort_reid.yaml]
5. Association
Containment algorithm assigns gear strictly to wearer box
[inference.py]
6. Safety Engine
10s sliding window (70% confirm / 30% clear) suppresses noise
[safety_engine.py]
7. Persistence
Annotated snapshot saved; incident logged to SQLite WAL
[event_manager.py]
8. Web Dashboard
Live WebSockets push compliance status & telemetry to UI
[websocket_hub.py]

## Slide 4
04 · EDGE IOT TIER
ESP32-CAM Hardware Architecture & Embedded Firmware
SITEGUARD · 04
AI-Thinker ESP32-CAM Node
• Microcontroller: Dual-core Xtensa 32-bit LX6 @ 240 MHz (AI-Thinker ESP32).
• Camera Sensor: Omnivision OV2640 2-Megapixel CMOS sensor with hardware JPEG encoding.
• Memory Subsystem: 520 KB internal SRAM + 4 MB external PSRAM for double buffering.
• Wireless Connectivity: Integrated 802.11 b/g/n Wi-Fi (2.4 GHz) link to Host Server.
• Host Machine Profile: AMD Ryzen 5 5625U CPU (integrated Radeon Graphics), running FastAPI + SQLite.
• Power Requirements: 5V DC stabilized external power supply (common ground).
Firmware & HTTP Ingestion (velxio.cpp)
⚡ Paced Frame Interval: 5 FPS (200 ms loop pacing, counting transmission latency).
⚡ Resolution & Compression: QVGA (320x240) JPEG at quality factor 12 (crisp, small payload).
⚡ PSRAM Double Buffering: config.fb_count = 2 in PSRAM with CAMERA_GRAB_LATEST: captures next frame while uploading current frame.
⚡ HTTP Socket Reuse: http.setReuse(true) keep-alive skips fresh TCP handshake per frame.
⚡ Self-Healing Telemetry: Camera init retries every 2s on failure; Wi-Fi auto-reconnects on RF drop.
⚡ Heartbeat Telemetry: Reports device_id, Wi-Fi RSSI, free heap, and uptime to /api/camera/heartbeat.

## Slide 5
05 · COMPUTER VISION TIER
CLAHE Contrast Enhancement & YOLOv8n Gated Detection
SITEGUARD · 05
Luminance-Preserving CLAHE
• 1. Buffer Decoding: cv2.imdecode parses incoming JPEG bytes into a standard BGR NumPy array.
• 2. BGR to CIE LAB: Separates Luminance (L) from chromatic channels (A and B). This preserves vibrant PPE colors (orange/neon yellow) without color shift.
• 3. Adaptive CLAHE on L: clipLimit = 2.0, tileGridSize = (8, 8). Boosts local contrast in harsh shadows, backlit scaffolding, and dawn/dusk lighting while capping noise amplification.
• 4. Letterboxing: Converted back to BGR; aspect-ratio padded to 640x640 px for neural input.
• Benchmark Speed: <4.2 ms execution per frame on Ryzen 5 CPU; zero ingestion bottleneck.
YOLOv8n & Asymmetric Confidence Gates
🎯 Architecture: Ultralytics YOLOv8n (Nano) anchor-free single-stage detector (~6.2 MB).
🎯 10 Active Classes: Person, Hardhat, NO-Hardhat, Vest, NO-Vest, Mask, NO-Mask, Cone, machinery, vehicle.
🎯 Tighter NMS IoU (0.40): Eliminates duplicate overlapping boxes (Ultralytics default is 0.70).
🎯 Person Gate: 0.35: Low threshold ensures workers are never missed even under distance or occlusion.
🎯 Worn PPE Gate: 0.40: Hardhat, Safety Vest, Mask: balanced threshold for worn gear.
🎯 Violation Gate: 0.50: NO-Hardhat, NO-Safety Vest, NO-Mask: higher threshold suppresses false alarms.

## Slide 6
06 · ASSOCIATION & IDENTITY
BoT-SORT Deep Re-ID & Spatial Containment Association
SITEGUARD · 06
BoT-SORT Tracking with Deep Re-ID
• The Limitation of Motion-Only: Kalman filter trackers (ByteTrack / SORT) lose identity when workers cross paths or stop moving behind scaffolding.
• Deep Visual Embeddings: with_reid: True extracts deep appearance vectors for every detected worker box.
• Global Motion Compensation: gmc_method: sparseOptFlow cancels camera vibrations and wind movement.
• Appearance Threshold (0.75): High cosine similarity bar prevents false ID swaps between workers wearing similar gear.
• Track Buffer (45 frames): Maintains lost tracks for >9 seconds at 5 FPS to reconnect re-emerging workers.
Bounding Box Containment Matching
CONTAINMENT(B_PPE, B_Person) = Area(B_PPE ∩ B_Person) / Area(B_PPE)
Threshold: >= 0.50 (at least 50% of PPE box must lie inside Person box)
✔ Multi-Worker Disambiguation: When workers stand side-by-side, each PPE item belongs strictly to the worker bounding box that contains it.
✔ Floor / Scaffold Drop: Loose PPE lying on the ground or scaffold matches nobody and is automatically discarded.
✔ Conflict Resolution: If both Hardhat and NO-Hardhat land on the same worker, the higher confidence score wins.
✔ Atomic Worker Checklist: Produces a per-worker checklist bound to the track_id: {'helmet': ('ok', 0.82), 'vest': ('missing', 0.74)}.

## Slide 7
07 · SAFETY ENGINE
Dual-Threshold Temporal Hysteresis & Incident Dispatch
SITEGUARD · 07
10-Second Hysteresis Rule Engine
• Sliding Window Buffer: Tracks each worker's PPE observations over a 10.0-second sliding window (requires >=3 frames).
• Confirmation Threshold (70%): An item is confirmed missing only when absent in >=70% of frames over the full window.
• Clearance Threshold (30%): A violation is cleared only once missing share drops to <=30%.
• Zero Alert Flapping: The 40% hysteresis gap prevents alerts from toggling on and off during momentary head turns or occlusion.
• Single-Episode Incidents: Raises exactly ONE incident when an episode starts; new missing items update it; no duplicate alerts.
Incident Lifecycle & Dispatch
🔔 Evidence Snapshot Saving: Saves annotated JPEG evidence snapshot to data/evidence/ immediately upon violation confirmation.
🔔 Non-Blocking SQLite WAL: Uses PRAGMA journal_mode=WAL and PRAGMA synchronous=NORMAL for concurrent ACID logging.
🔔 Severity Tiers: Helmet missing: HIGH | Vest missing: HIGH | Mask missing: MEDIUM.
🔔 WebSocket Real-Time Push: Broadcasts 'INCIDENT_ALERT' payload to all connected dashboard sessions in sub-50 ms.
🔔 Dynamic Parameter Overrides: Every threshold is configurable via SITEGUARD_* environment variables or live dashboard sliders (no server reboot).

## Slide 8
08 · SYSTEM VALIDITY
Safety Reliability Scorecard & Empirical Benchmarks
SITEGUARD · 08
OVERALL SAFETY RELIABILITY SCORE: 91.25 / 100 (GRADE A+)
Composite Formulation: Score = (0.35 · S_det) + (0.25 · S_lat) + (0.20 · S_up) + (0.20 · S_dup)
Detection Reliability (35%)
85.0 / 100
Worker & PPE precision/recall on complex site video footage.
Latency Performance (25%)
90.0 / 100
Average inference latency 48.2 ms on consumer Ryzen 5 CPU.
System Uptime (20%)
95.0 / 100
ESP32 node heartbeat continuity and automatic recovery.
Duplicate Suppression (20%)
100.0 / 100
Single-incident episode state management eliminates noise.
Load Benchmark Results (tools/benchmark_system.py):
Tested with 2–4 concurrent cameras streaming @ 5 FPS. Async queue prevented handler blocking with 0 dropped frames and sub-100 ms end-to-end latency.

## Slide 9
09 · LITERATURE JUSTIFICATION
Benchmark Matrix: 15 Research Papers Backing SiteGuard
SITEGUARD · 09
Built Capabilities (11 Papers)
✔ BoT-SORT (Aharon 2022): Re-ID appearance embeddings + GMC tracking
✔ ByteTrack (Zhang 2022): Low-score detection box association
✔ YOLOv8 (Jocher 2023): Single-stage PAN-FPN anchor-free detector
✔ CLAHE (Zuiderveld 1994): Luminance adaptive contrast equalization
✔ PPE Containment (Fang 2018): Two-stage spatial bounding box attribution
✔ Hysteresis (Sultani 2018): Dual-threshold temporal voting eliminates flicker
✔ Edge-Cloud IoT (Satyanarayanan 2017): Tiered architecture: capture nodes + edge host
✔ Tail at Scale (Dean 2013): Async queuing with drop-stale latency mitigation
✔ ARIES / WAL (Mohan 1992): Write-Ahead Logging for non-blocking DB writes
✔ ONNX Runtime (Microsoft 2020): Graph optimization for 2-4x faster CPU inference
✔ OSNet Re-ID (Zhou 2019): Multi-scale feature extraction for person Re-ID
Roadmap & Future Scope (4 Papers)
🚀 Struck-By Proximity (Ray & Teizer 2012) · PARTIAL 2D machinery/vehicle classification active. Roadmap: 3D metric Euclidean distance calculation via calibrated camera homography.
🚀 TinyML on Node (David 2021) · PLANNED Ultra-lightweight quantized person-presence filter directly on ESP32 to eliminate streaming empty frames.
🚀 Pose Estimation (Cao 2019 / OpenPose) · PLANNED Skeleton keypoint analysis to detect worker falls from height and unsafe ergonomic postures.
🚀 Closed-Loop IoT Actuation (Al-Fuqaha 2015) · PLANNED Bi-directional telemetry enabling server to trigger physical sirens/buzzers and LED beacons on the ESP32 node.

## Slide 10
10 · DEPLOYMENT & VISION
Production Deployment, IoT Expansion & Summary
SITEGUARD · 10
Production Deployment Pathways
• Local Host (Current MVP): ESP32-CAM to local PC (FastAPI + YOLOv8n + SQLite WAL). Zero cloud cost, sub-50 ms latency, no internet needed.
• Edge Gateway (Jetson Orin Nano): Deploy TensorRT FP16/INT8 on an onsite fanless edge box handling 8+ IP RTSP streams.
• Hybrid Cloud (AWS ECS + Triton): Edge nodes stream to AWS ECS cluster with Triton Inference Server; long-term analytics stored on S3.
• Containerized Docker Suite: Docker Compose stack (fastapi-core, nginx, redis, postgres) for one-click deployment at site offices.
Executive Summary & Achievements
★ Full Edge-to-Host Pipeline: Operational wireless ESP32-CAM (5 FPS) ingestion to real-time FastAPI inference engine.
★ BoT-SORT Deep Re-ID: Appearance embeddings overcome occlusion ID swapping when workers cross paths.
★ Zero Alert Flapping: Spatial containment (>=50%) and 70/30 temporal hysteresis produce exactly one alert per violation episode.
★ A+ Safety Grade (91.25/100): Empirically validated with sub-50 ms inference latency and 100% duplicate alert suppression.
★ Rigorous Scientific Backing: Architecture and algorithms benchmarked against 15 seminal computer vision & IoT papers.
Thank You! • Questions & Discussion