## Slide 1
AI-BASED SAFETY MONITORING
AI-Based Personal Protective Equipment (PPE) Compliance Monitoring System for Construction Sites Using Embedded Vision and IoT
Real-time AI-based PPE detection, worker tracking, and safety monitoring — from camera feed to live dashboard.
Manual monitoring cannot continuously observe every worker
Computer vision detects PPE violations automatically
Confirmed incidents flow live to a safety dashboard
NAME PRN
Shivam Shivange 123B1C064
Akhilesh Mohorir 123B1C048
Vinayak Pawara 123B1C032
Nrupendra Kulkarni 123B1C016
DEPT :- MDM - IOT
Branch :- CSE(AIML)
Project Guide : Dr. S. L. Tade

## Slide 2
SYSTEM METHODOLOGY
End-to-End Architecture Flow
Camera /
ESP32-CAM
Wi-Fi
PC Server
YOLO
Detection
React
Dashboard
Incident
Management
Safety Rule
Engine
ByteTrack
CAMERA / ESP32-CAM → WI-FI → PC SERVER → YOLO → BYTETRACK → SAFETY RULES → INCIDENT → DASHBOARD

## Slide 3
PIPELINE STAGE 1
Data Acquisition & Preprocessing
Camera
PC webcam for prototyping, or ESP32-CAM as the IoT capture device.
Wi-Fi Transmission
ESP32-CAM streams captured frames to the PC server over Wi-Fi.
Frame Capture
The server receives and decodes incoming image data continuously.
OpenCV Processing
Resize, preprocess, and control frame rate before inference.
Frame Preparation
Cleaned frames (5-10 FPS) are handed to the AI detection model.
Camera captures 25-30 FPS; AI inference runs on a reduced 5-10 FPS to cut unnecessary compute.

## Slide 4
PIPELINE STAGE 2
AI Detection & Worker Tracking
Input Frame
YOLO Model
Person + Helmet
+ Vest
ByteTrack
Worker IDs
Tracking lets the system reason about individual workers over time, instead of treating every frame as brand new.
DETECTION OUTPUT
Person #12 Helmet → Detected Vest → Detected
Safety Goggles → Detected
Person #18 Helmet → NOT DETECTED Vest → Detected
Safety Goggles → Detected
Each object carries a bounding box, class, and confidence score every frame.

## Slide 5
PIPELINE STAGE 3
Safety Rule Engine & Violation Confirmation
Detection
Raw per-frame YOLO output for a tracked worker.
Tracking
Worker identity held consistent across frames.
Persistence Check
Violation must hold across consecutive frames.
Cooldown / Duplicate Check
Prevents repeat alerts for the same ongoing event.
Violation Confirmed
A genuine incident is created, not a false alarm.
WORKED EXAMPLE
Worker #12
↓
No Helmet
↓
Persistent (6+ frames)
↓
Confirmed Incident
A single missed-frame detection never creates an incident on its own — only a persistent, confirmed violation does.

## Slide 6
PIPELINE STAGE 4
Incident Management & Real-Time Dashboard
Confirmed
Violation
Incident
Creation
Evidence
(Screenshot/Clip)
FastAPI /
WebSocket
React
Dashboard
CONSTRUCTION SAFETY DASHBOARD
24
Workers
92%
Helmet Compliance
88%
Vest Compliance
3
Active Violations
RECENT SAFETY INCIDENTS
⚠ Worker #12 — No Helmet ⚠ Worker #07 — No Safety Vest

## Slide 7
ROADMAP
Testing, Deployment & Future Scope
1
PC Webcam
2
Software
Prototype
3
ESP32-CAM
4
Real Construction
Footage
5
Cloud / Edge
Deployment
TESTING FOCUS
Model accuracy — precision, recall, mAP, F1
Tracking stability — ID consistency, ID switches
False alarms, missed & duplicate violations
Latency, frame rate, CPU/GPU & network load
Reliability — low light, occlusion, weather
FUTURE SCOPE
Restricted-zone entry & machinery proximity
Fall detection & unsafe posture
Multi-camera monitoring across a site
Edge AI & cloud deployment for scale
Advanced analytics — trends, heatmaps, risk
Prototype performs AI-based safety monitoring on a PC/server today, with ESP32-CAM as the planned IoT camera layer.
Development Flow :-