## Slide 1
SITEGUARD
AI-Based Construction Site Worker Safety Monitoring System
Edge-IoT Ingestion • YOLOv8n Detection • BoT-SORT Deep Re-ID • Temporal Hysteresis Rule Engine
Capstone Project Technical Presentation • Local Host / Edge Architecture

## Slide 2
CONTEXT & CHALLENGES
Construction Safety Problem & Core Objectives
Industry Safety Hazards
• Fatalities & High Non-Compliance: Construction accounts for 20%+ of workplace fatalities; failure to equip hardhats and vests is the #1 citation.
• Manual Monitoring Bottlenecks: Safety officers cannot monitor multiple video feeds continuously; fatigue causes missed non-compliances.
• False Alarm Fatigue: Raw single-frame CV detectors trigger rapid false alarms on momentary occlusions and sensor noise.
• Equipment Hazard Proximity: Ground workers traversing blind spots near heavy excavators and trucks without active spatial tracking.
SiteGuard System Objectives
✔ Autonomous Edge Ingestion: Stream low-latency QVGA/VGA frames from wireless ESP32-CAM nodes over Wi-Fi at 5 FPS.
✔ Accurate PPE Attribution: Simultaneous detection of workers and safety gear with strict bounding-box spatial containment (IoU >= 0.50).
✔ Identity Preservation via Re-ID: Track workers across prolonged occlusions using BoT-SORT appearance embeddings and Kalman filtering.
✔ Temporal Verification (Zero Flapping): Require 70% missing PPE persistence over a 10s sliding window before raising an incident.
✔ Real-Time Dashboard & Telemetry: Instant WebSocket broadcast, evidence snapshot recording, and SQLite WAL database logging.

## Slide 3
ARCHITECTURE OVERVIEW
End-to-End System Dataflow & Modular Services
1. Ingestion
ESP32-CAM / Webcams stream raw JPEG over HTTP POST at 5 FPS
2. Preprocessing
CIE LAB color space conversion + Luminance CLAHE enhancement
3. Vision Model
YOLOv8n (640x640) inference detects Person, PPE & Machinery
4. Re-ID Tracker
BoT-SORT preserves worker track IDs across visual occlusions
5. Spatial Match
Containment algorithm assigns PPE boxes to enclosing worker body
6. Safety Engine
10s sliding window (70% confirm / 30% clear) suppresses noise
7. Persistence
Evidence JPEG stored; SQLite WAL records incident episode
8. WebSocket UI
Broadcasts live worker compliance matrix & alerts to Dashboard

## Slide 4
HARDWARE & EDGE CONNECTIVITY
ESP32-CAM IoT Node & Pinout Configuration
ESP32-CAM Specifications & Firmware
• SoC Processor: AI-Thinker ESP32-CAM, Xtensa Dual-Core 32-bit LX6 @ 240 MHz.
• Camera Sensor: Omnivision OV2640 2MP CMOS; QVGA/VGA streaming @ 5 FPS.
• Memory Subsystem: 520 KB internal SRAM + 4 MB external PSRAM for double buffering.
• Buffer Management: config.fb_count = 2 in PSRAM with CAMERA_GRAB_LATEST mode.
• HTTP Client Optimization: Persistent TCP connection with http.setReuse(true) keep-alive.
• Heartbeat Telemetry: Periodic transmission of Wi-Fi RSSI, camera ID, and free heap.
AI-Thinker GPIO Hardware Interconnect
⚡ Power & Reset: PWDN -> GPIO 32 | RESET -> -1 (Unused) | 5V DC stabilized VCC
⚡ Clock Signals: XCLK -> GPIO 0 (20 MHz) | PCLK -> GPIO 22
⚡ Sync Signals: VSYNC -> GPIO 25 | HREF -> GPIO 23
⚡ SCCB I2C Interface: SIOD (SDA) -> GPIO 26 | SIOC (SCL) -> GPIO 27
⚡ 8-Bit Parallel Bus: Y2: GPIO 5, Y3: GPIO 18, Y4: GPIO 19, Y5: GPIO 21 Y6: GPIO 36, Y7: GPIO 39, Y8: GPIO 34, Y9: GPIO 35
⚡ Wireless RF: 802.11 b/g/n 2.4 GHz link connecting to FastAPI PC Host Server

## Slide 5
COMPUTER VISION PIPELINE
Image Preprocessing & CLAHE Luminance Normalization
1. Color Space Shift
CIE LAB Transformation • Frame decoded into BGR array. • Converted to CIE LAB via cv2.COLOR_BGR2LAB. • Separates Luminance (L-channel) from Chrominance (A & B channels). • Preserves worker PPE color fidelity (safety orange/neon yellow) without tint distortion.
2. CLAHE Equalization
Adaptive Contrast Boosting • Applied strictly to L-channel. • Clip Limit = 2.0 to prevent noise overamplification. • Tile Grid Size = (8, 8) for localized enhancement. • Recovers hidden workers and PPE under harsh shadows, scaffolding backlighting, and dawn/dusk lighting.
3. Letterbox & Normalization
Model Preparation • Converted back to BGR space. • Optional 3x3 Gaussian smoothing to soften JPEG compression noise. • Padded aspect-ratio letterboxing to 640x640. • Execution benchmark: <4.2 ms on Ryzen 5 CPU, ensuring zero ingestion bottlenecks.

## Slide 6
DETECTION ARCHITECTURE
YOLOv8n Specifications & Confidence Gates
Model Architecture & Weights
• Architecture: Ultralytics YOLOv8n (Nano) Single-Stage Anchor-Free Detector.
• Model Weight File: yolov8n_v1_best.pt (~6.2 MB) / ONNX Runtime FP32.
• Inference Resolution: 640 × 640 pixels (optimal resolution/compute tradeoff).
• Feature Extractor: Cross-Stage Partial DarkNet with Path Aggregation Network (PAN).
• NMS IoU Threshold: Tighter 0.40 threshold (Ultralytics default: 0.70) suppressing duplicate person/vest bounding boxes.
• Dual Runtime Support: Native PyTorch or ONNX Runtime (2–4× throughput gain on CPU).
Class Taxonomy & Asymmetric Gates
🎯 Person (Gate: 0.35): Low threshold ensures workers are never missed even under distant or partially occluded views.
🎯 NO-Hardhat, NO-Vest, NO-Mask (Gate: 0.50): High threshold suppresses false positive violation alerts.
🎯 Hardhat, Safety Vest, Mask (Gate: 0.40): Balanced threshold detecting equipped safety gear reliably.
🎯 machinery & vehicle (Gate: 0.45): Localizes excavators, cranes, trucks, and forklifts on site.
🎯 Safety Cone (Gate: 0.40): Identifies restricted physical boundary delineations.

## Slide 7
MULTI-OBJECT TRACKING
BoT-SORT Tracker with Deep Appearance Re-ID
Why Deep Re-ID is Crucial
• The Kalman Filter Limit: Pure motion trackers (ByteTrack / SORT) lose tracks if workers stop moving or cross paths closely.
• Visual Occlusions: Workers passing behind pillars or machinery undergo ID switching without visual feature memory.
• Deep Visual Embeddings: Extracts appearance feature vectors capturing clothing, gear color, and aspect ratios.
• Cosine Similarity Association: Re-identifies returning workers by matching appearance memory even after 45+ frames of total occlusion.
BoT-SORT Implementation (botsort_reid.yaml)
⚙ with_reid: True: Enables deep appearance feature extraction per detected worker bounding box.
⚙ gmc_method: sparseOptFlow: Global Motion Compensation computes background optical flow to cancel out camera shaking/vibration.
⚙ appearance_thresh: 0.75: High cosine similarity threshold preventing false identity swaps between workers in similar vests.
⚙ track_buffer: 45 frames: Maintains lost worker states alive for >9 seconds at 5 FPS to reconnect re-emerging workers.
⚙ fuse_score: True: Fuses detection confidence score with visual Re-ID cost matrix.

## Slide 8
PPE-WORKER ASSOCIATION
Geometric Bounding Box Containment Algorithm
Association Formulation
Mathematical Definition:
Containment(B_PPE, B_Person) = Area(B_PPE ∩ B_Person) / Area(B_PPE)
• Bounding box containment requires at least 50% (PPE_CONTAINMENT_MIN = 0.50) of the PPE box to lie inside the worker box. • Solves the multi-worker attribution problem when two workers stand side-by-side. • Loose PPE detections on floors or scaffolding belonging to no worker are discarded.
Conflict Resolution & Per-Worker State
✔ Max-Confidence Arbitration: If a worker has both 'Hardhat' and 'NO-Hardhat' boxes associated, the detection with the higher confidence score wins.
✔ Worker Checklist Generation: Produces an atomic per-worker PPE status dictionary: {'helmet': ('ok', 0.82), 'safety_vest': ('missing', 0.74)}.
✔ Track ID Coupling: All PPE states are bound to the worker's unique track_id, enabling historical temporal evaluation across frames.

## Slide 9
SAFETY RULE ENGINE
Dual-Threshold Temporal Hysteresis & Alert Cooldown
10-Second Sliding Window
Sliding Window Buffer • Maintains deque of observations per tracked worker. • Window duration: 10.0 seconds. • Minimum observations required: 3 frames before making any compliance verdict. • Worker records auto-expire after 10.0 seconds of absence from the scene.
Dual Confirmation Ratios
Hysteresis Gap • Confirmation Ratio: 70% (item confirmed missing only if absent in >=70% of frames over window). • Clearance Ratio: 30% (violation cleared only when missing frames drop <=30%). • The 40% gap completely eliminates alert flapping caused by momentary head turns or occlusion.
Single-Episode Incidents
Episode-Based Alerts • Exactly 1 incident created when violation begins. • If more items go missing (e.g. vest after helmet), existing incident updates. • Zero duplicate alerts during a continuous violation. • New alert generated only if worker clears and violates again later.

## Slide 10
EVALUATION & VALIDITY
Safety Reliability Scorecard & Performance Metrics
Composite Score Formulation
Weighted Scorecard Formula:
Score = (S_det × 0.35) + (S_lat × 0.25) + (S_up × 0.20) + (S_dup × 0.20)
• S_det (35%): Detection precision & recall on worker PPE. • S_lat (25%): Inference responsiveness (<100 ms on CPU). • S_up (20%): System uptime & camera heartbeat stability. • S_dup (20%): Duplicate suppression via episode tracking.
Operational Scorecard Results
★ Overall Score: 91.2 / 100 — Grade A+
★ Detection Reliability: 85.0 / 100
★ Latency Performance: 90.0 / 100 (Avg inference: 48.2 ms)
★ System Uptime: 95.0 / 100 (Zero crash daemon loop)
★ Duplicate Suppression: 100.0 / 100 (Zero duplicate incident rows)
★ Total Incidents Logged: 158 validated safety violations

## Slide 11
LITERATURE JUSTIFICATION
Benchmark Matrix: 15 Research Papers & Implementation Status
Paper / Author | Topic / Method | Scientific Justification | Status
BoT-SORT (Aharon 2022) | Re-ID + GMC Tracking | Deep appearance vectors prevent ID swaps across occlusions | IMPLEMENTED
ByteTrack (Zhang 2022) | Low-Score Box Tracking | Associates weak detection boxes to bridge occlusion gaps | IMPLEMENTED
YOLOv8 (Jocher 2023) | Anchor-Free Detection | PAN-FPN architecture enables 50ms real-time CPU inference | IMPLEMENTED
CLAHE (Zuiderveld 1994) | Luminance Contrast | Boosts dark/backlit outdoor frames without color distortion | IMPLEMENTED
Hierarchical PPE (Fang 2018) | Spatial Containment | Two-stage containment attributes PPE strictly to worker body | IMPLEMENTED
Hysteresis Anomaly (Sultani 2018) | Dual-Threshold Window | Eliminates single-frame detection flickering and false alerts | IMPLEMENTED
Edge-Cloud IoT (Satyanarayanan 2017) | Tiered Architecture | Partitions capture nodes (ESP32) and local edge server | IMPLEMENTED
Machinery Zones (Ray & Teizer 2012) | Struck-By Proximity | 2D machinery detection active; 3D metric Euclidean distance | ROADMAP / PARTIAL

## Slide 12
DEPLOYMENT & ROADMAP
Production Deployment Options & Future Enhancements
Deployment Options
• Option 1: Local Host (Current): PC Server (Ryzen 5 CPU) running FastAPI + YOLO + SQLite WAL. Zero cloud cost, sub-50ms latency.
• Option 2: Edge Gateway (Jetson Orin Nano): Migrate to FP16/INT8 TensorRT on an onsite fanless edge box handling 8+ IP RTSP streams.
• Option 3: Hybrid Cloud (AWS ECS / Triton): Centralized multi-site oversight across nationwide construction projects with cold-storage analytics on S3.
• Option 4: Containerized On-Premise Suite: Docker Compose bundle (fastapi-core, nginx, redis, postgres) for plug-and-play onsite setup.
Roadmap & Future Capabilities
🚀 3D Metric Proximity Zones: Calculate Euclidean ground distances using calibrated pinhole camera homography rather than 2D bounding boxes.
🚀 On-Node TinyML Filtering: Deploy a quantized person-presence wake-up detector directly on ESP32 before network transmission.
🚀 Skeleton Pose Estimation: Integrate YOLOv8-pose to classify slips, trips, falls from height, and ergonomic risk factors.
🚀 Bi-Directional IoT Actuation: Reverse HTTP/MQTT commands triggering sirens and strobe LEDs on ESP32 GPIO 4 during critical violations.

## Slide 13
SiteGuard: Summary of Achievements
✓ End-to-End Edge-to-Host Pipeline with ESP32-CAM (5 FPS) and FastAPI Backend
✓ YOLOv8n + BoT-SORT Deep Appearance Re-ID resolving visual occlusion ID swaps
✓ Spatial Containment (IoU >= 0.50) with Dual-Threshold Temporal Hysteresis (70%/30%)
✓ Validated 91.2/100 Safety Score (Grade A+) with Zero Duplicate Incident Flapping
✓ Rigorous Benchmark of 15 Research Papers Supporting All Architectural Choices
Thank You! • Questions & Discussion